## Slide 1: VERILOG
- Sidharth Magoon
Placed @ Synopsys ;Internship @ Mentor :P

## Slide 4: Need

## Slide 5: VHDL and Verilog

## Slide 6: Simulation and Synthesis
Simulation- to verify functional correctness of design
Synthesis- design modelled into implementation consisting of gates
Non synthesizable constructs like tasks,delay, event , fork-join etc

## Slide 7: HDL Simulators
ModelSim- Mentor
VCS- Synopsys
NC Sim/ Incisive- Cadence
Vivado- Xilinx

## Slide 8: Resources
Verilog HDL- Samir Palnitkar
Verilog LRM
Morris Mano

## Slide 9: Let’s Begin !
Design Methodologies top –down & bottom –up
Modelling Styles-
Gate Level
Data Flow
Behavioral
Switch Level

## Slide 10: Gate level Modelling
And(f,a,b..)
Nand(f,a,b..)
Similarly or,nor,xor,xnor,not
Buf(f,a)
notif0(f,a,e)
notif1(f,a,e)
Bufif0(f,a,e)
Bufif1(f,a,e)

## Slide 11: More about Gates

## Slide 13: Gate level- Code
module my_and_gate(o,a,b);
output o;
input a,b;
and and1(o,a,b);
endmodule

## Slide 14: Ports
4 types of signal values 0,1,X,Z
Net/wire is just a connection
Reg –holds a value
All port declarations are wire by default
When modules instantiated in another
input must be wire
Output can be wire/reg , usualy reg
Inout must be net

## Slide 15: Testbench
module tb_my_and;
wire o;
reg a,b;
my_and_gate ma1(o,a,b);
initial begin
$monitor(“time =%d, o=%b,a=%b,b=%b”,$time,o,a,b);
end
initial begin
#10 a=1’b0; b=1’b1;
#10 a=1’b1; b=1’b0;
#10 a=1’b1; b=1’b1;
end
endmodule

## Slide 16: Testbench
$monitor is one of many system tasks
$time represents current simulation time
Initial block executed once at t=0
Always block
Bit format eg 5’b11100, 6’o57,3’d6,8’h2D etc

## Slide 17: Exercise 1
Create half adder design
Create it’s testbench and simulate
Create full adder module by using half adder module
Again create testbench and simulate

## Slide 18: Data Flow Modelling
Keyword assign results in continuous assignment
Bitwise operators
a=3’b001,b=3’b110
~a inverts each bit- 3’b110
a&b -and
a|b -or
a^b -xor
a~^b -xnor

## Slide 19: Half adder example
module half_adder(s,c,a,b);
output s,c;
input a,b;
assign s=a^b;
assign c=a&b;
endmodule

## Slide 20: Decoder example
module decoder_1 (f,x,y);
output [0:3] f;
input x,y;
assign f[0]=~x&~y;
......complete.....

## Slide 21: Vectors and arrays
Vectors- wire [0:2] wire1;
reg [3:0] reg1; etc
Arrays- allowed only for reg, integer ,time
reg mem[31:0] etc
What does reg [3:0] mem [31:0] mean?

## Slide 22: Wire types
wor, wand etc
Example
module test_wor();
wor a;
reg b,c;
assign a=b;
assign a=c;
initial begin
$monitor(“time=%d,a=%b,b=%b,c=%b”,$time,a,b,c)
end
Initial begin
#10 b=1’b0;
#10 c=1’b0;
#10 b=1’b1;
.......check...

## Slide 23: Arithemetic and logical operators
Arithmetic- +, -, *, / ,% ,** if any operand contains x or z , result is unknown
Logical operators
a=4, b=0
&& logical and a&&b=0
|| logical or a||b=1
!a =0

## Slide 24: Shift, relational and equality operators
Logical shifts
a=4’b0010
a>>1, a<<2
Arithmetic shifts
a=4’b1010
a<<<3, a>>>2

## Slide 25: Shift, relational and equality operators
Relational operators- result in x if any operand x or z, else they evaluate to 1 or 0
(a>b), (a>=b) etc

## Slide 26: Operators continued
Concatenation-
wire [3:0] a1;
wire abit;
wire [6:0] a2;
assign c= {a1,abit,a2};
Replication
assign c={4{abit},4’b0000};
Conditional *
assign y= (sel? A:B)//mux
assign y= (s1? (s0?i1:i2) : (s0? I3:i4)); //nesting

## Slide 27: Comparator
module comparator(comp,a,b);
output comp;
input [7:0] a,b;
assign comp = ((a>=b) ? 1’b1:1’b0);
endmodule

## Slide 28: Exercises
1. Design a four bit ripple carry adder (gate level modelliing)

## Slide 29: Exercises
2. Design a BCD adder, assume 4 bit inputs a &b , input carry c0 , and output sum and carry.
(using data flow modelling)

## Slide 30: Exercises
2.Design an ALU which implements the following
S0 S1 Output
0 0 a+b
0 1 a^b
1 0 a-b
1 1 a>>b
Assume a & b are of 2 bits each

## Slide 31: Delays
Regular delays
assign #d1 y= a&b;
Intra assignment delays
assign y= #d1 a&b;
Assign #d1 y= #d2 a&b;
Gate and net delays
wire #5 y1;
and #3 and1(y,x1,x2);

## Slide 32: Delays
Rise delay – transition from 0,x,z to 1
Fall delay – transition from 1,x,z to 0
Turn off delay?
and #(1,2,3) a1(....);
and #(2,5) a2(...);
Minimum, typical and maximum delays
and #(1:2:3,4:5:7) a3 (...)

## Slide 33: Timing Checks
Setup time , hold time ?
Violations?

## Slide 34: Behavioral Modelling
Always and initial block
--contain blocking and non blocking assignments(note not concurrent)
--may have sensitivity list
--contain all if-else statements and case statements(they cant exist without always/initial block)

## Slide 35: Day-2

## Slide 36: FINITE STATE MACHINES

## Slide 39: ‘10’ sequence detector

## Slide 40: Designing FSM Using Verilog “sequence-1101”

## Slide 41: STEPS
Assignment of states
Defining CLOCK
Next state function
Assignment of next state to current state
Output function

## Slide 42: Assignment of States
-Defining states by using PARAMETER
parameter s1=2’b00,s2=2’b01,s3=2’b11,s4=2’b10;
reg[1:0] Q,D; //present and next state

## Slide 43: CLOCK
reg clk;
initial clk<=0;
always
#20 clk<=~clk;

## Slide 44: State function
always@(x or Q)
begin
y<=0;
case(Q)
s1:D<=x?s2:s1;
s2:D<=x?s3:s1;
s3:D<=x?s3:s4;
s4:
if(x) begin
D<=s2;
y<=1;
end
else begin
D<=s1;
end
default:D<=2’bxx;
endcase
end

## Slide 45: Next state function
Assign next state to present state at clock edge (if reset then system goes to default => Q=0;)
?
?
?
?

## Slide 46: Output for Moore FSM
parameter s1=3’b000,s2=3’b001,s3=3’b011,s4=3’b110;
always@(Q)
y=Q[2];

## Slide 47: Generate statement
Work as parrallel block, allows instance creation
module Rcadder (a,b,ci,s);
parameter n=64;
input [n-1:0] a,b;
input ci;
output [n-1:0] s;
wire [n-1:0] pc;
genvar i;
generate for (i=0;i<n;i++) begin :u1
fulladder inst[i] (a[i],b[i],pc[i],s[i],pc[i+1]);
end
endmodule

## Slide 48: Tasks
Variables declared are local
Can include timing delays like @, # wait etc
Output assigned only at end of execution of task
A task must be clled within a statement
task task_name ;
input output variable declartions
local variables
procedural statements
endtask

## Slide 49: Functions
Behaves same as tasks but a difference
Cannot include timing delays like @, #,wait; hence used only for modelling of combinational ckts
Functions can call other functions but not other tasks
Can have any number of inputs but only 1 output
Unlike tasks they need to be called as part of expression

## Slide 50: Function example
function my_function;
input a,b,c,d;
begin
myfunction=((a+b)+(c-d));
end
endfunction
module function_calling(a,b,c,d,e,f);
output f;
input a,b,c,d;
`include “myfunction.v”
assign f= (myfunction(a,b,c,d))? e:0;
endmodule